## Slide 1: Introduction to Geographic Information Systems
Peter Galante
Biodiversity Informatics Scientist
Center for Biodiversity and Conservation
American Museum of Natural History

## Slide 2
Outline
How do we represent real world geographic information with a computer?
  What is a Geographic Information System?
  Data models – representations of geographic reality
  GPS
  Georeferencing, sampling bias
  Remote Sensing

## Slide 3
Notable GIS software
Commercial:
ArcGIS, including ArcMap (Esri)
IDRISI (Clark Labs)
ERDAS IMAGINE (ERDAS Inc.)
Open source:
Quantum GIS
GRASS GIS
MANIS tool
GPSvisualizer
Biogeomancer
Free (but not open source):
DIVA GIS

## Slide 4
What is a Geographic Information System?
A Geographic Information System (GIS)
  software, hardware, geographic information, spatially explicit data
Software can be used to store, query, manage, analyze and display spatial data.
A GIS links cartographic, statistical, and data-basing technologies.

## Slide 5
What is a Geographic information system?
Data (layers)
  Spatial – Images, shape data, geographic information
  Tabular – Spreadsheet data with geographic properties

## Slide 6
Layering

## Slide 7
Outline
How do we represent real world geographic information with a computer?
  What is a Geographic Information System?
  Data models – representations of geographic reality
  Georeferencing, sampling bias
  Remote Sensing

## Slide 8
Two methods of GIS representation
There are two main ways a GIS can create a logical data model of the world:
- Raster = continuous fields
- Vector = discrete features

## Slide 9
Two methods of GIS representation
There are two main ways a GIS can create a logical data model of the world:
- Raster = continuous fields
- Vector = discrete features

## Slide 10
Two methods of GIS representation
There are two main ways a GIS can create a logical data model of the world:
- Raster = continuous fields
- Vector = discrete features

## Slide 11
Vector
Discrete objects
  Represents the geographic world as objects with well-defined boundaries in otherwise empty space

## Slide 12
Vector
Discrete objects
  Represents the geographic world as objects with well-defined boundaries in otherwise empty space

## Slide 13
Vector
Discrete objects
  Represents the geographic world as objects with well-defined boundaries in otherwise empty space

## Slide 14
Vector Data
- Vector data represents features as points, lines, and polygons.
- It is best applied to discrete
objects with defined shapes
and boundaries.
- It is tied with tabular data
Examples include:
  GPS points
  Roads
  Protected areas

## Slide 15
Raster
Continuous fields
  Represents the real world as a finite number of variables, each one defined at every possible position.
E.g. a Digital Elevation Model

## Slide 16
Raster Data
A raster model represents the world as a surface that is divided into a regular grid of cells, each of which are assigned a value.
Raster data includes images and grids.
aerial photograph, a satellite image,
or a scanned map, are often used
for generating raster datasets.

## Slide 17
General data issues: spatial scale
Decrease in resolution
Increase in extent
Spatial scale has two elements: resolution and extent
Resolution
Extent
Resolution and extent tend to be
inversely related

## Slide 18
Vector data
Advantage
  precise representation of points, boundaries, and linear features
    defining spatial relationship (connectivity and adjacency) between coverage features
    network analysis (for example to find an optimal path between two nodes in a complex transport network)
Disadvantage
  boundaries of the resulting map polygons are discrete/enclosed by well-defined boundary lines. In reality the map polygons may represent continuous gradation or gradual change, as in soil maps
  Resolution is not clear – how many points were used to make up a line?

## Slide 19
Raster data
Advantage
  Represent indistinct boundaries
    thematic information on soil types, soil moisture, vegetation, ground temperatures
  Reconnaissance satellites and aerial surveys use raster-based scanners
    scanned images can be directly incorporated into GIS
Potential disadvantage
  The higher the grid resolution, the larger the data file is going to be
  If converting from vector to raster can lose information:

## Slide 20
Outline
How do we represent real world geographic information with a computer?
  What is a Geographic Information System?
  Data models – representations of geographic reality
  GPS
  Georeferencing, sampling bias
  Remote Sensing

## Slide 21
GPS

## Slide 22
Outline
How do we represent real world geographic information with a computer?
  What is a Geographic Information System?
  Data models – representations of geographic reality
  GPS
  Georeferencing, sampling bias
  Remote Sensing

## Slide 23
Species’ distribution data: possible sources
Personal collection during field surveys (e.g., using a GPS receiver or smartphone)
Extracting data from large surveys (e.g., North American Breeding Bird Survey)
Digitizing atlases (e.g. The new atlas of breeding birds in Britain and Ireland: 1988-1991)
Collections in natural history museums
On-line distributed databases (e.g. GBIF, HerpNET, FishNET, ORNIS)

## Slide 24
Georeferencing
Woodbury, NY
Near Woodbury
5 miles from Woodbury
1 mile east of Woodbury
10 minutes along the path leading out of Woodbury

## Slide 25
Outline
How do we represent real world geographic information with a computer?
  What is a Geographic Information System?
  Data models – representations of geographic reality
  GPS
  Georeferencing, sampling bias
  Remote Sensing

## Slide 26
What is remote sensing?
Source: P. Ersts, July 2004
General definition: Acquiring information about an object without physical contact.
Definition in context of Earth observation: A technology for sampling reflected and emitted electromagnetic (EM) radiation of features on the Earth's land surface, oceans, and atmosphere.

## Slide 27
GIS projects
The majority of your grade for this course will be based on a comprehensive final project. Ideally, your project will represent some aspect of your graduate research. It should be of sufficient quality to be used in a publication, whether as just a map (or series of maps), supporting documentation, or values generated as part of an analysis.
If you do not have a project, or an interesting spatial aspect of a project, we can chat and come up with one.